## Slide 1
Vision-Based Robotic Arm Teleoperation
Single-camera hand tracking mapped to servo commands through deterministic Python logic, configurable transport, and PCA9685-based firmware
Repo-verified prototype review
Host-side Python performs camera capture, hand tracking, feature extraction, filtering, and operator state logic.
Two board targets exist: Arduino Uno over serial and ESP32 DevKit V1 over Wi-Fi UDP.
Both firmware paths drive a PCA9685 and accept the same ASCII command packet.
The checked-in runtime profile currently targets ESP32 + UDP.
Prototype scope
This is a practical first integration prototype. It is not a closed-loop industrial manipulator, and the base is not angle-observed because it uses a continuous-rotation servo.
Current checked-in profile
Transport: UDP
Board: ESP32 Arduino + PlatformIO
Servo output: PCA9685 channels 0..4
Camera profile: 1280x720 at 30 FPS
Slide 1

## Slide 2
Repo Findings and Scope Boundaries
Vision Arm Teleoperation Prototype
Implemented now
Computed but inactive
Not present in source
Primary implemented system
Python teleop in main.py is the active host path. It uses MediaPipe landmarks, direct joint mapping, filtering, and a transport abstraction that can send the same command semantics over serial or UDP.
Whole-hand finger curl actively drives the gripper.
Direct joint mapping actively drives lower, middle, and upper pitch joints.
Both Uno and ESP32 firmware actively parse packets and drive the PCA9685.
The same ASCII TeleopCommand packet is shared across all active paths.
pinch_metric is computed and calibratable, but not used to actuate the gripper.
wrist_tilt_metric is computed and displayed, but not used to drive a joint.
map_workspace() exists, but the live loop does not call it.
Kinematics and workspace config fields remain, but the runtime is not using IK.
No active kinematics.py source file
No project send_fixed.py
No project main.c
No project-level Zephyr CMakeLists.txt
Important caveat
The deck should describe the current runtime as direct hand-to-joint teleoperation, not as inverse-kinematics task-space control.
Slide 2

## Slide 3
End-to-End System Overview
Vision Arm Teleoperation Prototype
Camera frame
OpenCV capture
MediaPipe Hands
21 landmarks
Feature extraction
center, depth, curl
Filtering + state
logic
TeleopCommand
ASCII packet
Firmware + PCA9685
servo outputs
The host owns perception, normalized signal generation, filtering, and operating-mode decisions.
The board firmware owns packet validation, watchdog behavior, calibration mapping, and final PWM output.
The transport boundary is intentionally narrow: one shared line-oriented command packet.
Current deployment choice
The architecture supports both serial and UDP. The checked-in calibration profile uses ESP32 + UDP, but the host-side control semantics remain the same across both transport paths.
Slide 3

## Slide 4
Hardware Architecture
Vision Arm Teleoperation Prototype
Host side
Laptop or host PC runs Python teleop stack.
Single RGB webcam is the primary perception sensor.
OpenCV window provides overlay and keyboard controls.
Current camera profile in calibration.json is 1280x720 at 30 FPS.
Board / drive side
Arduino Uno over serial remains implemented.
ESP32 DevKit V1 over Wi-Fi UDP is the current checked-in target.
Both firmware paths drive a PCA9685 at 50 Hz.
Servo channels 0..4 map to base, lower, middle, upper, gripper.
Actuation side
Continuous-rotation base yaw servo
Three pitch joints with gear reductions
One gripper servo
External servo power and common ground are documented assumptions
Documented wiring, not code-enforced
The repo documents ESP32 I2C as GPIO21/GPIO22 and Uno I2C as A4/A5. The firmware confirms the PCA9685 channel map, but physical wiring and power integrity still need hardware confirmation.
Slide 4

## Slide 5
Mechanical Command Model and Calibration Mapping
Vision Arm Teleoperation Prototype
Host commands lower, middle, and upper joints in output joint degrees, not raw servo degrees.
Firmware converts joint angles to servo angles using zero offsets, direction signs, and fixed gear ratios.
Current output limits are q1<=45°, q2<=60°, q3<=90°.
The continuous base is commanded around BASE_STOP_DEG with a configured speed range and neutral trim.
Current checked-in gripper endpoints are 0° closed and 180° open.
Firmware-side mapping
lower_servo = zero + sign × 4 × lower_joint
middle_servo = zero + sign × 3 × middle_joint
upper_servo = zero + sign × 2 × upper_joint
Generated header values in current profile
BASE_STOP_DEG = 90
BASE_HOLD_TRIM_COMMAND = 0.25
BASE_SPEED_RANGE_DEG = 28
SERVO_SLEW_DEG_PER_S = 120
Important caveat
The repo still stores richer geometry and kinematics parameters, but the live runtime does not currently use them for inverse kinematics.
Slide 5

## Slide 6
Software Stack and Library Roles
Vision Arm Teleoperation Prototype
Python host
Firmware
OpenCV handles camera capture, image mirroring, display, and overlay drawing.
MediaPipe Hands provides landmark detection and tracking for one hand.
NumPy handles distances, angles, normalization, and geometric feature computation.
pyserial implements the serial transport path; socket implements the UDP path.
dataclasses + JSON provide structured configuration and calibration persistence.
Arduino framework keeps both board targets simple and readable.
Wire provides I2C access to the PCA9685.
WiFi and WiFiUDP are used only in the ESP32 path.
Adafruit PWM Servo Driver Library generates servo PWM through the PCA9685.
PlatformIO builds the ESP32 Arduino target.
Branch separation
There is no active Zephyr application in this repo snapshot. The PlatformIO README files are template placeholders, not alternate firmware implementations.
Slide 6

## Slide 7
Vision Pipeline
Vision Arm Teleoperation Prototype
main.py opens the camera with DirectShow, applies the configured frame size/FPS, and sets CAP_PROP_BUFFERSIZE to 1.
If mirror_view is true, the frame is flipped before hand tracking so control uses mirrored image coordinates.
MediaPipe Hands runs with static_image_mode=false, model_complexity=1, and max_num_hands from config.
Candidates are filtered by requested handedness and a minimum normalized palm width threshold.
The tracker returns one HandObservation containing normalized landmarks, pixel landmarks, center_xy, and derived metrics.
Current profile values
max_num_hands = 1
min_detection_confidence = 0.45
min_tracking_confidence = 0.35
min_palm_width_norm = 0.015
Center definition
The hand center is the mean of landmarks [0, 5, 9, 13, 17], which approximates a palm center rather than using a fingertip or bounding-box center.
Accuracy caveat
This is monocular hand tracking. The landmark z values are relative model outputs, not metrically calibrated camera depth.
Slide 7

## Slide 8
Feature Extraction: Active Signals vs Computed Signals
Vision Arm Teleoperation Prototype
Actively used in control
Computed or stored, but inactive
x_offset_norm: hand horizontal displacement from a captured neutral x position
height_norm: hand height inside the active control box
depth_norm: normalized reach command derived from a heuristic depth metric
finger_curl_norm: normalized whole-hand closure used to command the gripper
pinch_metric is computed from thumb-tip to index-tip distance
wrist_tilt_metric is computed from the palm normal
wrist_tilt_reference is still captured and stored
pinch_open_reference and pinch_closed_reference are still captured and stored
map_workspace() exists, but the live loop does not call it
Depth proxy formula
depth_metric = 0.65 × palm_width + 0.25 × wrist_middle + 0.10 × mean_palm_depth
Gripper feature
finger_curl_metric blends joint-angle curl with fingertip folding distance and then combines all five fingers as 0.7 × mean + 0.3 × min.
Slide 8

## Slide 9
Teleoperation Mapping Math
Vision Arm Teleoperation Prototype
Base command = signed-deadband(x_offset_norm), then exponent shaping, then yaw_max scaling.
Lower joint target comes from depth_norm; the current profile inverts this mapping.
Upper joint target comes from height_norm.
Middle joint target is a weighted average of upper and lower; the current profile uses 0.5.
Joint norms are multiplied by q1_max, q2_max, q3_max to produce transmitted joint angles in degrees.
Gripper openness is thresholded: fully open below the open threshold, fully closed above the close threshold, proportional in between.
Current profile
yaw_deadband = 0.12
yaw_exponent = 1.5
gripper_full_open_threshold = 0.03
gripper_full_close_threshold = 0.5
Direct joint mapping, not IK
control_mode is present in config and set to direct_joint, but main.py does not branch on it. The checked-in runtime is explicitly direct hand-to-joint mapping.
Unused config caveat
middle_height_invert is present in config but not consumed by compute_joint_norms() in the current source.
Slide 9

## Slide 10
Filtering, Motion Conditioning, and Grasp Stabilization
Vision Arm Teleoperation Prototype
Low-pass filters smooth x, height, depth, and grip before state logic uses them.
Slew rate limiters cap the rate of change for lower, middle, upper, and gripper targets.
When the gripper is actively closing, arm-rate scaling drops to grasp_arm_slowdown_factor.
Depth hold freezes the depth signal when curl exceeds a threshold, then auto-releases after 6 seconds or when the hand reopens enough.
If tracking drops briefly, the host stays in hold for lost_hold_timeout_s before falling back to waiting-for-hand behavior.
Current filter profile
x_alpha = 0.35
y_alpha = 0.25
depth_alpha = 0.18
grip_alpha = 0.28
Current rate profile
joint_rate_deg_s = 95
gripper_rate_per_s = 1.8
grasp_arm_slowdown_factor = 0.2
Important precision note
This is signal conditioning and mode logic, not closed-loop control. There is no measurement of actual joint angle or gripper force in the current implementation.
Slide 10

## Slide 11
Runtime Modes and Operator State Logic
Vision Arm Teleoperation Prototype
Current startup profile enters a 1-second home phase first, because send_home_on_start is true.
After startup homing, the system remains frozen until the operator unfreezes it.
A mode is used for active teleop when a tracked hand is inside the active region.
H mode is used for frozen, waiting, and brief tracking-loss hold behavior.
S mode is the estop-hold command and is also force-sent immediately when estop toggles on.
M mode sends a home posture: zero joint angles plus the startup gripper opening fraction.
Operator controls
q quit
f / space freeze
x estop
h home
r reload config
Live calibration controls
n capture neutral
o capture open hand
p capture closed hand
[ ] trim base neutral
Behavior nuance
Hold and estop are posture-hold behaviors, not torque disable. The arm keeps its last commanded pose while the base is driven to a neutral-trim stop command.
Slide 11

## Slide 12
Transport and Packet Interface
Vision Arm Teleoperation Prototype
Shared packet
T,seq,mode,base_cmd,lower_deg,middle_deg,upper_deg,gripper_open
TeleopCommand.encode() is the source of truth for the line format and uses ASCII with a trailing newline.
SerialController and UdpController both rate-limit sends independently of camera frame rate.
force=True bypasses rate limiting for home and estop packets.
SerialController retries port open and provides strong diagnostics for common Windows serial conflicts.
UdpController treats socket creation as connected-enough and does not require a session handshake.
The host overlay surfaces transport status, but the main loop does not currently implement autonomous reconnect.
Current checked-in transport profile
transport.kind = udp
udp.host = 192.168.137.50
udp.port = 4210
udp.write_hz = 60
Serial profile remains implemented
serial.enabled = false in the checked-in profile, but the serial path still exists and uses the same command semantics at 30 Hz by default in calibration.json.
Diagnostic helper
send.py reuses TeleopCommand and can optionally wait for an ESP32 UDP reply after each test packet.
Slide 12

## Slide 13
Firmware Paths: Arduino Uno and ESP32
Vision Arm Teleoperation Prototype
Arduino Uno + serial
ESP32 DevKit V1 + Wi-Fi UDP
Parses the shared ASCII packet over Serial.
Uses PCA9685 channels 0..4 for the five actuators.
Applies watchdog hold, clamping, zero/sign/gear-ratio mapping, and slew limiting.
Lets very small base trim commands pass through without forcing the deadband break.
Parses the same ASCII packet over UDP port 4210.
Connects to Wi-Fi in station mode and uses a static IP from wifi_secrets.h.
Sends simple OK,seq,mode or ERR replies to the sender.
Applies watchdog hold, clamping, zero/sign/gear-ratio mapping, and slew limiting.
Currently applies base deadband directly, which differs slightly from the Uno path.
Why this matters
The host-side teleop semantics are intentionally preserved across both board targets. The transport changes; the meaning of the command does not.
Slide 13

## Slide 14
Calibration, UI, and Operator Workflow
Vision Arm Teleoperation Prototype
config/calibration.json is the master runtime and calibration source.
n captures neutral_x, neutral_y, depth_reference, and wrist_tilt_reference.
o and p capture both pinch references and grip-curl references.
The overlay shows status, transport, landmarks, joint targets, grip, finger curl, wrist tilt, and depth-hold state.
Host-side config changes can be reloaded live with r; firmware-side changes require header export and reflashing.
calibration.py can export both the Uno and ESP32 generated calibration headers.
Host-side live tuning
Region boundaries, neutral references, grip references, trim, and transport choice live in JSON and can be updated without rewriting host logic.
Firmware-side reflashing
Servo zeroes, signs, limits, base stop, slew, and gripper endpoints are exported into generated_calibration.h and then compiled into the board firmware.
Caveat
Pinch and wrist-tilt capture still exist in the workflow even though those features do not currently drive the live teleop mapping.
Slide 14

## Slide 15
Safety, Limitations, and Technical Value
Vision Arm Teleoperation Prototype
Safety and robustness present
Limitations to state plainly
Startup freeze prevents immediate free motion.
Active teleop requires a valid tracked hand inside the active region.
Brief tracking-loss hold avoids abrupt command drops on short perception failures.
Host and firmware both clamp or limit motion in different ways.
Firmware watchdog returns the arm to hold if packets stop arriving.
No joint encoders and no closed-loop state feedback
Base yaw is open-loop continuous-servo rate control
Depth is a heuristic monocular proxy, not metric 3D
The live runtime is direct joint mapping, not task-space IK
Some config and computed signals are inactive or only partially wired
Why this still matters technically
Prototype 1 already solves a hard integration problem: turning a noisy monocular hand-tracking pipeline into a stable actuator command stream with transport abstraction, firmware clamping, and an operator-visible calibration workflow.
Slide 15

## Slide 16
Roadmap: From Prototype 1 to a More Industry-Style System
Vision Arm Teleoperation Prototype
Move from hobby-servo assumptions to stiffer mechanics and higher-quality actuators.
Add encoders and actual joint-state measurement so motion can be closed-loop rather than purely open-loop.
Promote dormant geometry and workspace concepts into a real inverse-kinematics and trajectory-generation path.
Measure end-to-end latency and jitter explicitly, especially across the Wi-Fi path.
Separate timing-critical firmware work if complexity grows; RTOS partitioning becomes relevant only after tighter control requirements appear.
Add hardware safety interlocks, current/temperature limits, and richer fault handling.
Move toward custom electronics and sensor fusion once the manipulation objectives justify the added complexity.
Concrete meaning of 'closer to industry standard'
Measured state, calibrated kinematics, trajectory planning, timing visibility, fault handling, and hardware-level safety. The next step is not just a better mapping function; it is a better instrumented robot system.
Slide 16